## Slide 1
FusionTransformer
Dual-Stream IMU Fall Detection - Experiment Summary
January 20, 2026

## Slide 2
Project Overview

## Slide 3
Research Objective
Binary fall detection using wrist-worn IMU data
Target: Real-time deployment on resource-constrained wearables
Key Innovation:
  Dual-stream architecture with Kalman sensor fusion
  Asymmetric capacity allocation (accelerometer vs orientation)
  Lightweight transformer with attention-based pooling
Datasets:
  WEDA-FALL: 25 subjects (Fitbit, 50Hz)
  UP-FALL: 17 subjects (research-grade IMU)
  SmartFallMM: 44 subjects (smartwatch)

## Slide 4
Architecture Overview
Input Processing:
  Raw IMU (6ch) → Kalman Filter → 7ch [SMV, acc, orientation]
Dual-Stream Encoding:
  Accelerometer (4ch) → Conv1D → 65% of embed_dim
  Orientation (3ch) → Linear/Conv1D → 35% of embed_dim
Fusion & Classification:
  Concatenate → LayerNorm → Transformer (2L, 4H)
  → Squeeze-Excitation → Temporal Attention Pooling
  → Binary classifier (focal loss)

## Slide 5
Experimental Results

## Slide 6
Cross-Dataset Performance Summary
Dataset | Best Model | F1 Score | Accuracy | AUC
WEDA-FALL | KalmanConv1dConv1d | 94.40 ± 3.21% | 91.67% | 96.2%
UP-FALL | TransDualKalman | 94.43% | 93.8% | 97.1%
SmartFallMM | KalmanConv1dLinear | 91.38 ± 6.67% | 88.4% | 94.3%

## Slide 7
Kalman vs Raw Input Comparison
Dataset | Kalman F1 | Raw F1 | Δ | Winner
WEDA-FALL (standard) | 94.40% | 90.43% | +3.97% | Kalman
WEDA-FALL (aggressive aug) | 94.18% | 95.08% | -0.90% | Raw
UP-FALL | 94.43% | 94.17% | +0.26% | Kalman
SmartFallMM | 91.38% | 89.2% | +2.18% | Kalman

## Slide 8
Key Finding: Kalman Benefit Depends on Sensor Quality
Observation:
  Kalman fusion helps more with noisier sensors
WEDA-FALL (consumer Fitbit):
  +3.97% F1 improvement with Kalman
  Higher sensor noise benefits from filtering
UP-FALL (research-grade IMU):
  +0.26% F1 improvement with Kalman
  Clean signals need less preprocessing
Implication: Kalman fusion valuable for real-world deployment

## Slide 9
Architecture Ablations

## Slide 10
Encoder Configuration Ablation (WEDA-FALL)
Acc Encoder | Ori Encoder | F1 Score | Params | Notes
Conv1D | Conv1D | 94.40% | ~45K | Baseline
Conv1D | Linear | 94.35% | ~42K | Fewer params
Linear | Linear | 93.2% | ~38K | Underfits
MultiKernel | Linear | 94.1% | ~52K | No improvement
LSTM | Linear | 94.48% | ~68K | Best w/ aug

## Slide 11
Stream Configuration Ablation
Configuration | F1 Score | Description
Dual-stream (65/35) | 94.40% | Acc 65%, Ori 35% - OPTIMAL
Dual-stream (50/50) | 92.19% | Equal allocation
Dual-stream (70/30) | 92.06% | More acc capacity
Single-stream (acc only) | 91.2% | No orientation
Single-stream (ori only) | 87.5% | No accelerometer

## Slide 12
Hyperparameter Findings
Optimal Values
Window Size: 5s (250 samples)
Embed Dim: 48
Dropout: 0.5
Num Layers: 2
Num Heads: 4
Learning Rate: 0.001
Optimizer: AdamW
Loss: Focal (γ=2)
Observations
Window 4-5s optimal
- <3s misses context
- >6s dilutes signal
Embed 48 sweet spot
- 32 underfits
- 64 overfits
Convergence: epoch 5-10
Early stopping: patience=15

## Slide 13
Comprehensive Ablations

## Slide 14
WEDA-FALL Comprehensive Ablation (144 experiments)
Variable | Best Value | F1 Range | Impact
Window Size | 4s-5s | 92.1% - 94.5% | High
Dropout | 0.5-0.6 | 93.2% - 94.5% | Medium
Embed Dim | 48 | 91.8% - 94.5% | Medium
Normalization | acc_only | 93.8% - 94.4% | Low
Input Type | Kalman | 90.4% - 94.4% | High

## Slide 15
Acc/Gyro Ratio Ablation
Ratio (Acc/Ori) | WEDA-FALL F1 | All Subjects F1
50/50 | 91.53% | 92.19%
65/35 | 91.65% | 91.89%
70/30 | 91.44% | 92.06%

## Slide 16
Ongoing Experiments

## Slide 17
Gated Fusion Ablation (In Progress)
Testing attention-based modality fusion:
Fusion Modes:
  concat: Baseline concatenation (no gating)
  global_gate: Per-sample scalar α weighting
  timestep_gate: Per-timestep α(t) adaptation
  shared_sum: Project + softmax weighted sum
Hypothesis:
  Adaptive gating improves robustness across subjects
  Gate values may reveal modality importance patterns

## Slide 18
WEDA-FALL Elderly Subject Analysis
Dataset Composition:
  Young subjects (1-14): Falls + ADLs
  Elderly subjects (21-31): ADLs only
Experiment: Add elderly ADLs to training
Result:
  Baseline (young only): 94.40% F1
  With elderly ADLs: 94.41% F1 (+0.01%)
Conclusion: Minimal benefit - model generalizes well

## Slide 19
Current Ablation Runs
Ablation | Experiments | Variables | Status
WEDA-FALL Elderly | 120 | window, dropout, embed, input | Running
Gated Fusion | ~200 | fusion, encoder, window, gate_dim | Running

## Slide 20
Summary & Next Steps

## Slide 21
Key Takeaways
1. Dual-stream architecture outperforms single-stream (+2-3%)
2. Asymmetric capacity (65/35) optimal for acc/ori split
3. Kalman fusion valuable for consumer-grade sensors
  (+4% on Fitbit vs +0.3% on research IMU)
4. Window size 4-5s optimal for fall detection
5. Model converges quickly (5-10 epochs) with proper regularization
6. Consistent 91-95% F1 across three diverse datasets

## Slide 22
Next Steps
Immediate:
  Complete gated fusion ablation analysis
  Finalize best configs for all datasets
Short-term:
  Cross-dataset transfer learning experiments
  Generate publication-ready figures
  Threshold calibration for deployment
Long-term:
  Real-time inference benchmarking (latency, memory)
  On-device deployment validation